## Slide 1: Synopsis of the prototype parabolic trough
Phil Ferrer
Khaled Mohammad
University of the Witwatersrand

## Slide 2: Custom Parabolic Trough System: Design, Collaboration & Operation
What is a Parabolic trough?
Specialized mirror structure (Diemaster industry)
Precision manufacturing in physics workshop
Tilting capability: Up to 45°
Closed-loop oil circulation
Vacuum system minimizes convective losses.
Real-time monitoring via IoT

## Slide 3: Key Parameters of the Prototype
Name | Value | Description
L | 4.42 m | Receiver Length
a | 2.4 m | Aperture Width
f | 1.3 m | Focal Length
δ | 0.3 m | Trough Height
ψ | 45° | Rim Angle
d1 | 0.056 m | Absorber Pipe (Inner)
d2 | 0.06 m | Absorber Pipe (Outer)
d3 | 0.08 m | Receiver Cover (Inner)
d4 | 0.084 m | Receiver Cover (Outer)
Rcol | 0.88 | Mirror Reflectivity (Visible)
Rcavity | 0.9 | Cavity Reflectivity (IR)
Io | 900 W/m² | Solar Irradiance
θ | 0.0 | Incident Angle
ṁ | 0.2 kg/s | Mass Flow Rate
CP | 2288.6 J/kg·K | Specific Heat (Genheat 22)
μ | 1.155×10⁻³ kg/m·s | Viscosity (Genheat 22)
koil | 0.128 W/m·K | Thermal Conductivity
V | 1.5–2.6 m/s | Wind Speed

## Slide 4: Mirrors and Optics
Mirror configuration functional, not optimized.
Windowed Receiver
Miro 4 (~95% reflectance)
Outdoor exposure led to damage
~19% optical reduction (surface damage)
Pixel analysis (~51% incident)
Total solar radiation efficiency at receiver: ~35% ± 4%.

## Slide 5: Pump Selection and IoT-Based Control System
Hebei Shenghui Pump Co., Ltd.
Max oil temperature: 350°C, Flow rate: 1.5 m³/h, Power: 0.75 kW, Efficiency: ~30%
Thermal oil: GENHeat 22, operating up to 255°C
Overflow system implemented
IoT-Based Control and Data Logging:
Web-based user interface connected to cloud database
Microcontrollers: HKD WEMOS LOLIN ESP32 (Wi-Fi)
Sensors (K-type thermocouples) inlet/outlet temp
Controllers for actuator, pump, and vacuum system
Data -> Google Firebase for real-time logging & control

## Slide 6: Receiver Design and Construction
Initial concept
Diemaster design
Physics workshop
Infrared mirror inset into housing;
Receiver pipe added concentrically and sealed with glass cover.
Borate silicate glass panels

## Slide 7: Theory: Heat Transfer in Solar Receiver Prototype
Prototype model similar
Vacuum levels insufficient (~103 Pa) ->convective heat losses (DMODEL!)
HTF flows in a closed loop:
1) Receiver section (RED: heated by solar radiation).
2) Loop pipe (YELLOW: insulated return path).
Temp flow profile (HT coefficient U)

## Slide 8: Heat Transfer Analysis: Receiver and Reconnection Pipe
Roil,conv
Rcond,ann
Rcond,inner
Rconv,ann
Rconv,outer
Rrad,outer
Rcond,outer
Rrad,ann
T
Tamb

## Slide 9: Cooling Cycle Analysis
Cooling cycle without solar input
HTF previously heated to ~136°C, circulated through receiver and loop pipe
Model temperature drop and heat loss
Parameters affecting heat loss
Curve fitting: U = 0.14 W/(m²·K), with R² = 0.98
Tout: 57°C, ~ measured value

## Slide 10: Heating Cycle Analysis
Heating cycle (baseline)
HTF heated by solar radiation at receiver and loses heat through loop section
Mass flow rate ṁ = 0.15 kg/s
±10% solar input shown
Dip due to cloud cover
Chart: Heating data vs simulation
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
Optimal +10% | 43 | 49.7402 | 56.2532 | 62.5464 | 68.6274 | 74.5033 | 80.1811 | 85.6673 | 90.9685 | 96.091 | 101.0406 | 105.8233 | 110.4448 | 114.9103 | 119.2252 | 123.3947 | 127.4235 | 131.3164 | 135.078 | 138.7127 | 142.2249 | 145.6186
Optimal -10% | 43 | 48.3129 | 53.4467 | 58.4073 | 63.2006 | 67.8323 | 72.3077 | 76.6322 | 80.8108 | 84.8485 | 88.7501 | 92.52 | 96.1628 | 99.6827 | 103.084 | 106.3705 | 109.5461 | 112.6147 | 115.5798 | 118.4448 | 121.2133 | 123.8883 | 126.4732
Optimal =294 K | 43 | 48.9638 | 54.7264 | 60.2947 | 65.6752 | 70.8743 | 75.898 | 80.7522 | 85.4427 | 89.9751 | 94.3546 | 98.5863 | 102.6754 | 106.6265 | 110.4444 | 114.1335 | 117.6982 | 121.1427 | 124.471 | 127.687 | 130.7946 | 133.7973 | 136.6988
Data | 43.65 | 49.4 | 56.15 | 60.8 | 66.2 | 71.4 | 76.6 | 81.9 | 86.15 | 91 | 94.4 | 93.9 | 93.4 | 92.9 | 93.4 | 99.9 | 112.4 | 121.15 | 124.9 | 128 | 130.15 | 132.9

## Slide 11: Impact of Thermal Insulation on Receiver Heat Loss
Convective losses: key factors
Insulation reduces surface temp and convective losses.
Insulation: cost-effective alternative to vacuum
Simulation results:
1 cm insulation: Tout = 37°C
2 cm insulation: Tout = 33°C
Chart: Temperature on insulated receiver
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
1cm insulation | 43 | 49.2282 | 55.3308 | 61.3103 | 67.1692 | 72.91 | 78.535 | 84.0466 | 89.447 | 94.7385 | 99.9233 | 105.0035 | 109.9813 | 114.8587 | 119.6378 | 124.3204 | 128.9087 | 133.4044 | 137.8094 | 142.1256 | 146.3548 | 150.4987
no insulation | 43 | 49.078 | 54.951 | 60.6259 | 66.1094 | 71.408 | 76.5278 | 81.475 | 86.2554 | 90.8745 | 95.3378 | 99.6506 | 103.8179 | 107.8447 | 111.7357 | 115.4954 | 119.1284 | 122.6388 | 126.0308 | 129.3084 | 132.4755 | 135.5358
Data | 43.65 | 49.4 | 56.15 | 60.8 | 66.2 | 71.4 | 76.6 | 81.9 | 86.15 | 91 | 94.4 | 93.9 | 93.4 | 92.9 | 93.4 | 99.9 | 112.4 | 121.15 | 124.9 | 128 | 130.15 | 132.9
2cm insulation | 43 | 49.2992 | 55.4944 | 61.5873 | 67.5794 | 73.4726 | 79.2685 | 84.9685 | 90.5745 | 96.0878 | 101.51 | 106.8427 | 112.0872 | 117.2451 | 122.3178 | 127.3067 | 132.2132 | 137.0387 | 141.7844 | 146.4517 | 151.0419 | 155.5563

## Slide 12: Impact of Vacuum Failure on Receiver Efficiency
Vacuum system achieved ~5 kPa, -> Convective heat transfer dominates
IR mirror reflectivity inside receiver high (but ineffective)
Total HTF heating efficiency from solar radiation: ~31% (~659 W/m).
Receiver heat retention efficiency: ~69% , ~89% (1 cm insulation), ~94% (2 cm insulation).
Efficiency approaches commercial units (e.g., PTR70 at ~95%).
Diminishing returns observed with increasing insulation thickness.

## Slide 13: Conclusively…
OPTIONS:
Improve Vacuum system (cost, power, maintenance, performance)
Test insulation around receiver (may make IR mirror redundant)
Change direction (include thermodynamic cycle)